## Slide 1
Lecture 1: How is switch changing the world?

## Slide 2: Impact of Electronics
Internet
Supercomputer
Visual Reality
Artificial Intelligent
Self-Driving
Personal
Industry
Healthcare
~$500 billion market in 2019

## Slide 3: Everything Starts with Switch
Information Processing Based on 0 and 1
0 1
Key features of a switch
On/Off
ON  Short circuit  a piece of conducting wire. OFF  Open circuit  an open gap in the circuit.
Control
On and off states of a switch can be controlled.

## Slide 4: Switch Examples
Mechanical Switches
Relay
Clumsy
Slow
Not Electronic

## Slide 5: The First Computer (1832)
Babbage’s Difference Engine
25,000 parts.
Cost: ￡17,500
Weight: 6 tons
1/7 completed, operated on 6-digit numbers and second- order differences.
Cannot perform a conditional branch – NOT Turing Machine

## Slide 6: The First Digital Computer (1941)
Zuse Z3
2,000 relays
22-bit word length
5-10 Hz
Not fully electronic
No conditional branch instruction*.
Practically, Z3 is not equivalent to
modern computers.
Device: Electro-mechanical relay

## Slide 7: Vacuum Tube & ENIAC
17468 vacuum tubes, 7200 diodes,
1500 relay
5000 +/- op/s, 385 * op/s
2.4 m  0.9 m  30 m, area size: 167 m2, weight: 27 t, Power: 150 KW
Longest Operation Time: 116 hr.

## Slide 8: Ge Point Contact Transistor
John Bardeen
William Shockley
First Ge-based point-contact transistor exhibited oscillator behavior, a critical test to prove the existence of power in December 1947. – A new age has come.
Walter Brattain

## Slide 9: Classification of Solids
Insulator
Metal
No conduction at all!
Always OFF
Current cannot be controlled Always ON
Semiconductor
Conduction occurs in certain conditions OFF ON

## Slide 10: The Chosen One - Silicon

## Slide 11: The Chosen One - Silicon
Sand Pile
Amorphous
Si Wafer
Single Crystalline

## Slide 12: Electrons and Holes
When freed from a covalent bond, an electron leaves a “void” behind because the bond is now
incomplete. The “void” is called a “hole”.
An electron-hole pair is generated when an electron is freed from the bond; an electron-hole recombination occurs when an electron falls into a hole.
ni is strongly dependent on temperature! -> Not good for applications

For intrinsic semiconductor, n0 = p0 = ni :
Boltzmann distribution:
Eg kBT

n 2  n p  N N e
i 0 0 C V

## Slide 13: Dope the Silicon Wafer

## Slide 14: n-type Si vs. p-type Si
+
-
n-type
p-type
region of
interest
P atom’s outmost orbit has 5 electrons.
“donor”: a n-type dopant with an “extra” valence electron and can easily donate an electron to the conduction band, and
P+
leaves a positive atom at local
position.
B atom’s outmost orbit has 3 electrons.
“acceptor”: a p-type dopant with a “missing” valence electron and can easily donate a hole to the valence band, and leaves a negative B- atom at local position.

## Slide 15: Two Terminal Electronic Switch - Diode
OFF
ON
OFF
ON
Need Three-Terminal
The switch mechanism is manipulated by electrical field
-> Transistor
Passively controlled by the biased voltage!

## Slide 16: The Final Winner - MOSFET
With the increase of Vgs
Hole
On/Off
On-state: carrier channel formed, where the current can flow
Off-state: carrier channel does not exist, no path for current to pass
Control
Actively controlled by electrical field
Most importantly, MOSFET can be scaled down!
Electron
- - - - - - - -
VG > 0
Large

## Slide 17: The Final Winner - MOSFET
Complementary MOS (CMOS)
Digital
Analog
Memory
CMOS is the driving engine for Info. Sci. & Tech.!
To drive the unprecedented revolution of the information era
Economical Scaling from sizes to nanometer – Moore’s Law

## Slide 18: Evolution of the Transistor
Modern IC
1947, bipolar transistor, Bell Lab
1958, First IC, Texas Instruments
1904, Vacuum tube